## Slide 1: Synthetic GOES-R Imagery of Agricultural and Wild Fires Eight Symposium on Fire and Forest Meteorology 13-15 October 2009, Kalispell, Montana Louie Grasso(1) , Renate Brummer, Robert DeMaria Cooperative Institute for Research in the Atmosphere, Fort Collins, Colorado Don Hillger NOAA/NESDIS/STAR/RAMMB, Fort Collins, Colorado (1) Corresponding author address: Lewis D. Grasso, CIRA/Colorado State University, 1375 Campus Delivery, Ft. Collins, CO 80523-1375 email: grasso@cira.colostate.edu

## Slide 2
MOTIVATION
1) To extend the operational use of the satellite by producing synthetic GOESR-ABI before the satellite is put into orbit.
2) The only way to examine temporal sampling is through the use of a numerical cloud model.
GOALS
1) Demonstrate we can create realistic synthetic GOESR-ABI imagery.
2) Use synthetic imagery for product development.
3) Use synthetic imagery for model evaluation.
Synthetic Imagery

## Slide 3: Creating Synthetic Imagery
Numerical cloud models: RAMS and WRF-ARW
RAMS/WRF-ARW Microphysics
  Two-moment cloud microphysics (RAMS: Meyers/WRF-ARW: Morrison)
  • Mass mixing ratio and number concentration are prognosed.
    RAMS: Pristine ice, snow, aggregates, graupel, hail, rain, small cloud drops, and large cloud drops.
    WRF-ARW: Ice, snow, graupel, rain, cloud drops.
  Two-way interactive nested grids
  Four grids: 50 km, 10 km, 2 km (GOES-R), and 400 m (NPOESS).
Run cloud model and use output as input to an observational operator to generate synthetic GOES-11, GOES-12, and GOES-R satellite observations at different channels.

## Slide 4
Observational Operator
  Community Radiative Transfer Model (CRTM) code used to calculate gaseous transmittances
  Modified anomalous diffraction theory (MADT) for cloud optical properties for λ > 3.9 µm
  Look-up tables for optical properties for λ <= 3.9 µm
  Delta-Eddington formulation for IR bands
  Spherical Harmonics Discrete Ordinate Method (SHDOM) for Vis and Near IR bands
    Plane parallel version (1-D) of SHDOM from CU (F. Evans)
A point spread function is applied to 400 m data to build the appropriate GOES-R ABI footprint size.

## Slide 5: Synthetic 2 km ABI Bands 7-16 8 May Severe Weather Case (19 UTC)
3.9 µm 6.2 µm 7.0 µm 7.3 µm
8.5 µm 9.6 µm 10.35 µm 11.2 µm
12.3 µm 13.3 µm

## Slide 6: Synthetic Fire Imagery
Acquire WF_ABBA retrieved fires and use the lat/lon to position fire hotspots within model domain.
Run simulated atmosphere with fire hotspots through SHDOMPP to produce synthetic 3.9 µm imagery.
This is done on a grid with 400 m horizontal grid spacings.
Apply appropriate GOES-R ABI point spread function on 400 m data to “build” appropriate GOES-R footprint.

## Slide 7
Left: MODIS Aqua 1 km true-color image for 23 October 2007 (created by NASA); Right: Synthetic ABI 3.9 µm image produced for 23 October 2007 at 1530 UTC.
Examples of synthetic GOES-R ABI 3.9 µm images with fires for (left) Southern California and (right) southern Yuctan.
Point spread function applied to 400 m data.
Point spread function applied here.
Use to develop a fire retrieval algorithm

## Slide 8
MODIS image at 1920 UTC on 15 April 2008 over southeastern Kansas. The background image is at 3.959 µm depicting two GOES-R saturated fire pixels within the small boxes. Both of the small boxes have been magnified and are shown as the larger boxes to the left. To the right is the corresponding magnified image at 2.13 µm. Arrows are used to identify the white saturated fire pixels at 3.959 µm and the corresponding black unsaturated fire pixels at 2.13 µm.
GOES-R ABI 2.25 µm for fire retrieval when 3.9 µm saturates?
Observational Motivation

## Slide 9
Idealized hotspots: Hotspots get larger from left to right; hotspots get hotter from bottom to top
Synthetic 3.9 µm GOES-R
Synthetic 2.25 µm GOES-R
White pixels: saturated Black pixels: unsaturated

## Slide 10
Southern California on 23 October 2007.
IDEALIZED SMOKE ADDED 

## Slide 12
Collaborations
Thank You!
Synthetic GOES-R ABI imagery at 3.9, 10.35, and 11.2 µm is being used at to aid in the development of WF_ABBA a fire detection and retrieval algorithm. (CIMSS: Jay Hoffman, Chris Schmidt)
Synthetic GOES-R ABI imagery may be used to aid in development of algorithms aimed at emissions from fires and retrievals of optical depths of smoke. (NOAA/NESDIS: Shobha Kondragunta, Xiaoyang Zhang)
Additional collaborations are welcome!

## Slide 13
<number>
Grasso, L. D., M. Sengupta, and M. DeMaria, 2009: Comparison between Observed and Synthetic 6.5 and 10.7 µm GOES-12 Imagery of Thunderstorms that occurred on 8 May 2003. Int. J. of Remote Sensing. In press.
Zupanski, D., M. Zupanski, L. Grasso, R. Brummer, I. Jankov, D. Lindsey, M. Sengupta and M. DeMaria, 2009: Assimilating synthetic GOES-R radiances in cloudy conditions using an ensemble-based method. Int. J. of Remote Sensing., Accepted with revision
Grasso, L. D., D. Lindsey, 2009: An Example of the use of Synthetic 3.9 µm GOES-12 Imagery for Two-Moment Microphysical Evaluation. Int. J. of Remote Sensing., Accepted with revision
Grasso, L. D., M. Sengupta, J. F. Dostalek, R. Brummer, and M. DeMaria, 2008: Synthetic satellite imagery for current and future environmental satellites. Int. J. of Remote Sensing., Vol 29, No. 15, 4373-4384.
Lindsey, D. T. and L. D. Grasso, 2007: An effective radius retrieval for thick ice clouds using GOES. J. Appl. Meteor. Climatol., Vol 47, 1222-1231.
Evans, K. F., 1998: The spherical harmonics discrete ordinate method for three-dimensional atmospheric radiation transfer. J. Atmos. Sci., 55, 429-446.
Grasso, L. D., and T. Greenwald, 2004: Analysis of 10.7 µm brightness temperatures of a simulated thunderstorm with two-moment microphysics. Mon. Wea. Rev., 132, 815-825.
Hillger, D.W., and J.D. Clark, 2002: Principal Component Image analysis of MODIS for volcanic ash, Part-1: Most important bands and implications for future GOES Imagers, J. Appl. Meteor., 41(10), 985-1001.
References
Notes: Interim accomplishments needed to reach the expected outcomes.