## Slide 1: Washington Volcanic Ash Advisory Center
Presented by Jamie Kibler
Notes: <number>

## Slide 2: Washington VAAC Volcano Program History
The volcanic ash monitoring program at the Satellite Analysis Branch (SAB) became official with a MOA agreement with the FAA in 1987 although volcano monitoring began in the 1970s for the entire world.
The Washington VAAC was established in 1997. The United States, in agreement with the International Civil Aviation Organization (ICAO), has designated the National Environmental Satellite Data and Information Services (NESDIS), Satellite Analysis Branch (SAB), and the National Weather Service (NWS) National Center for Environmental Prediction (NCEP) as the regional Washington Volcanic Ash Advisory Center (VAAC).
Washington VAAC began using the NCEP – Advanced Weather Interactive Processing System (N-AWIPS) in 2003 for the issuance of Volcanic Ash Advisories (VAAs) and Volcanic Ash Graphics (VAGs).
Notes: <number>

## Slide 3: Washington VAAC Organization
NOAA
    (National Oceanic and Atmospheric Administration)
NWS
NESDIS
(National Weather Service)
(National Environmental Satellite, Data and Information Service)
NCEP (National Centers for Environmental Prediction) Central Operations
SAB
Washington VAAC
(Satellite Analysis Branch)
Notes: <number>

## Slide 4: Washington VAAC Customers
Washington
VAAC
ACCs,
FAA
Pacific NW WFOs
MWOs
other
VAACs
VAAC = Volcanic Ash Advisory Center
MWO = Meteorological Watch Office
WFO = Weather Forecast Office
AWC = Aviation Weather Center
FAA = Federal Aviation Administration
  Other U.S. government agencies including AWC, DoD (AFWA), FEMA
DoD = Department of Defense
AFWA = Air Force Weather Agency
FEMA = Federal Emergency Management Agency
ACC = Area Control Center
Abbreviations:
Airlines,
Aviation community
Notes: <number>

## Slide 5: Washington VAAC Volcano Program
Washington VAAC area of responsibility includes the continental US, southward through Central America, the Caribbean, to 10S in South America and the US controlled oceanic Flight Information Region (FIR).
Washington is 1 of 9 VAACs that cover the globe. Other VAAC’s include Anchorage, Buenos Aires, Darwin, London, Montreal, Tokyo, Toulouse and the Wellington.
Monitoring volcano’s 24 hours a day 365 days a year
Washington VAAC is backup to the Montreal and Anchorage VAAC during disruptions in operations.
Air Force Weather Agency (AFWA) is the Washington VAAC backup during disruptions in operations.
Notes: <number>

## Slide 6: VAAC Boundaries
Wellington
Darwin
45
30
15
0
15
30
45
60
60
75
90
105
120
135
150
165
180
165
150
135
120
105
75
60
60
45
45
30
30
15
15
0
75
90
Tokyo
Washington
Montreal
London
Anchorage
Buenos
Aires
Toulouse
Notes: <number>
By 1997 the International Civil Aviation Organization (ICAO) divided the world’s airspace into nine Volcanic Ash Advisory Centers (VAAC). NOAA has the responsibility for 2 VAAC’s, Anchorage, Alaska (managed by the National Weather Service) and Washington (a cooperative effort between NESDIS and NWS)

## Slide 7: Washington VAAC Volcano Products
Volcanic Ash Advisory (VAA) which contains satellite information, reports of volcanic ash and a possible ash forecast. VAAs are advisory in nature and are meant to complement and support, but not replace, meteorological and aviation related warnings which includes Significant Meteorological Hazard Advisory (SIGMETs), and Notice to Airmen (NOTAMS).
Volcanic Ash Graphic (VAG) – A graphic depiction of ash over an 18 hour period showing extent, movement and size. Graphic is only provided when ash is seen in satellite imagery.
Volcanic Ash Forecast Transport and Dispersion model (VAFTAD) showing ash dispersion over a 48 hour period. VAFTAD’s are usually needed with multiple plumes, high ash heights or ash expected to last beyond +06 hours.
Notes: <number>

## Slide 8: Volcanic Ash Advisory
FVXX21 KNES 311614
VOLCANIC ASH ADVISORY ISSUED: 20070131/1614Z
VAAC: WASHINGTON
VOLCANO: SOUFRIERE HILLS 1600-05
LOCATION: N1642 W06210 AREA: W_INDIES
SUMMIT ELEVATION: 3002 FT (915 M)
ADVISORY NUMBER: 2007/091
INFORMATION SOURCE: GOES-12. GFS WINDS. RADIOSONDE. MONTSERRAT OBSERVATORY. PILOT REPORT.
ERUPTION DETAILS: REPORTED ASH AT 31/1540Z
OBS ASH DATE/TIME: 31/1545Z OBS ASH CLOUD: SFC/FL060 N1701 W06247 - N1643 W06210 - N1653 W06253 - N1700 W06255 - N1701 W06247 MOVING W 10-15 KNOTS.
FCST ASH CLOUD +6H: 31/2200Z SFC/FL060 10NM WIDE LINE BETWEEN N1651 W06304 - N1642 W06210.
FCST ASH CLOUD +12H: 01/0400Z SFC/FL060 10NM WIDE LINE BETWEEN N1651 W06305 - N1642 W06210.
FCST ASH CLOUD +18H: 01/1000Z SFC/FL060 10NM WIDE LINE BETWEEN N1641 W06306 - N1643 W06211.
REMARKS: AIRCRAFT REPORT OF ASH FROM FL050-060. MVO REPORTS LOW ACTIVITY OVER PAST 24 HOURS. A THIN PLUME CAN BE SEEN EXTENDING 50 NMI MOVING TO THE WNW AT 10-15 KTS. CONTENTS OF PLUME MAY CONTAIN ASH. NO HOTSPOT CAN BE SEEN IN SATELLITE IMAGERY. WILL CONTINUE TO MONITOR. ...SPAMPATA
NEXT ADVISORY: WILL BE ISSUED BY 20070131/2215Z
Notes: <number>

## Slide 9: Volcanic Ash Advisory
VAAs are available to the aviation community under headers FVXX## KNES (where ## denotes a number in the range 20-27) via a variety of communications systems, including Satellite Broadcast (e.g., WAFS, SADIS) and Global Telecommunications Network (GTS). VAA are also available via Aeronautical Fixed Telecommunications Network (AFTN).
VAAs also available via the internet at:
www.ssd.noaa.gov/VAAC/washington.html and
a listserv (to subscribe see: www.ssd.noaa.gov/VAAC/subscribe.html
NAWIPS – DBNET
VAGs are only available at this time by the internet or DBNET.
Notes: <number>

## Slide 10
http://www.ssd.noaa.gov/VAAC/messages.html
http://www.ssd.noaa.gov/SSD/LISTS/volc-list.html - Main page
Notes: <number>

## Slide 11
http://www.ssd.noaa.gov/VAAC/vaac.html
Notes: <number>

## Slide 12: Volcanic Ash Graphic
Available only by internet for now at http://www.ssd.noaa.gov/VAAC/messages.html
Notes: <number>

## Slide 13: HYSPLIT Model Volcanic Ash Cloud Forecast Guidance
http://www.ssd.noaa.gov/VAAC/vaftad.html
VAFTADs for the last 15 days
Notes: <number>

## Slide 14: Satellite Imagery Used
Washington
VAAC
GOES, POES, MTSAT
& Meteosat IR
GOES & POES
CIRA products
AURA-OMI
GOES PCI
(Principle
Component
Image )
GOES, POES, MTSAT
+ Meteosat Visible
  GOES & POES Ellrod Product
GOES, POES & MTSAT Channel Differencing
Product
* Have and use zoom capabilities for all imagery
GOES, POES, MTSAT
& Meteosat shortwave IR
Overlays
Boundaries – Countries, Airspaces
Winds – Cloud motion, soundings , and models
Volcano locations
Notes: <number>

## Slide 15: Prototype OMI Volcanic SO2 Website
http://gp16.ssd.nesdis.noaa.gov/pub/OMI/OMISO2/
Notes: <number>

## Slide 16: AURA-OMI – Detection of SO2
OMI- Ozone Monitoring Instrument – Part of the EOS AURA Mission
http://gp16.ssd.nesdis.noaa.gov/pub/OMI/OMISO2/
Notes: <number>

## Slide 17: Incoming Information Used (non-satellite)
Washington
VAAC
Airlines
Cable TV
Phone
News
reports
  e-mail,
variety of
Internet
sites
SIGMETs,
MWOs
GTS,
FOS,
phone,FAA AFTN
PIREPs
Weather
Observations
GTS,
FOS
AFTN=Aeronautical Fixed
Telecommunications Network
ATC=Air Traffic Control
  other
  VAACs
Phone
GTS,
Phone
to GTS, FOS
Phone, fax
FOS=Family of Services
GTS=Global Telecommunication System
USGS=U.S. Geological Survey
Abbreviations:
Volcanologists
(Observatories,
USGS, Smithsonian)
Volcano
cameras
  Infrasound data
Numerical Weather
& Dispersion Models
Notes: <number>

## Slide 18: Volcanic Ash Advisory Issuance
Detection of Ash in Satellite Imagery
The issuance of a SIGMET by an Meteorological Watch Office (MWO)
Pilot reports (Pireps) of ash with confirmation from MWO’s, Observatories and/or other points of contact.
Volcano Observatories (VO) and other related science facilities.
Other agencies such as AWC, AFWA, DOD etc.
Notes: <number>

## Slide 19: Process of Issuing a Volcanic Ash Advisory
Receive information from source
Send out Quick VAA
Issue Volcano Checklist which involves calling different agencies and writing down specifics of information
Make calls for additional information if needed.
Run Hysplit model if applicable
Notes: <number>

## Slide 20: Process of Issuing an Volcanic Ash Advisory
Issue full VAA with graphic and forecast.
Issue additional VAAs based on new information and/or updated forecast.
Continue to monitor for ash in satellite imagery, possible change in direction, or clouds break as ash is now able to be seen.
Continue to update agencies with additional information.
Notes: <number>

## Slide 21: VAA Cancellation
Ash is not detected in satellite imagery and clouds are not present. Volcano analyst is able to get a clear view of the volcano and surrounding region.
MWO office relays to VAAC they are ending SIGMETs as information provided to them signifies volcano is no longer erupting and ash has dissipated.
MWO SIGMET has expired although information is not provided to the VAAC – usually wait 12-24 hours after the expired SIGMET.
Notes: <number>

## Slide 22: Volcano Stats 2004-2008
2004
Total number of VAAs - 932
Graphics - 220
2005
Total number of VAAs - 2192
Graphics - 978
2006
Total number of VAAs - 1927
Graphics - 665
2007
Total number of VAAs - 1637
Graphics - 457
2008
Total number of VAAs - 1300
Graphics - 338
Notes: <number>