## Slide 1
by
Jb (SHyMet)

## Slide 2
Small rough pieces of volcanic glass, rock, or minerals ranging from 0.001 to 2.00 millimeters in size.
Composed largely of Silica (SiO2) or Rhyolitic (felsic – silica rich) minerals.
Volcanic ash is not formed during a combustion process, but as a result of a “explosive process.”
It is hard, (mostly)insoluble in water, rough, and corrosive.
07/29/26
<number>

## Slide 3
Volcanic ash forms during explosive eruptions when gases dissolved in the molten rock and under great pressure, expand and escape violently into the air. The force of the escaping gas then fiercely shatters the airborne, solidifying rocks.
Once in the air, and due to buoyancy effects, the hot ash (and other escaping gases) quickly rises and forms an eruption column that often reaches to more than 30,000 feet in elevation.
07/29/26
<number>

## Slide 4
Over the last 25 years, more than 100 jet aircraft sustained damage after flying through volcanic ash clouds. The repairs cost more than $250 million. At least 7 of these encounters resulted in temporary engine failure, with 3 aircraft losing power from all engines. These engine failures have occurred at distances ranging from 150 to 600 miles from the erupting volcano. Aircraft damage from these volcanic ash encounters has been reported from as far as 1,800 miles from the volcano.
07/29/26
<number>

## Slide 5
Volcanic ash damages windshields, windows, and external probes that tell pilots their airspeed and altitude, and can ruin antennae for communication and navigation radios. Ash can almost instantly contaminate onboard electronic equipment, air conditioning, equipment cooling systems, the fuel system, and hydraulic systems that move flight controls and extend landing gear.
07/29/26
<number>

## Slide 6
Operating temperatures in the engines can exceed 1400 C, melting ash particles which then deposit on turbine blades or clog fuel lines.
07/29/26
2

## Slide 7
The ash particles also damage the aerodynamic surfaces of aircraft, generally an insidious threat.
Damage to the windscreen is a very common occurrence. Documentation of the frequency and cost of such damage helped spur alert system development.
Coordinated efforts at volcano observatories, forecast offices and air traffic control centers began in the middle ‘90’s.
07/29/26
<number>

## Slide 8
07/29/26
<number>

## Slide 9
07/29/26
<number>
Common Routes of some of the 100,000 flight per year in this area.

## Slide 10
Many eruptions occur in uninhabited areas, undetected.
Ash clouds can remain airborne for several days.
Spreading of the plume reduces the visual signature and makes discrimination from clouds difficult, particularly at night.
Aircraft radar is ineffective.
07/29/26
<number>

## Slide 11
Eruptive volcanic plumes occur in numerous forms, varying in height, intensity, duration and in style.
A forced jet occurs at the surface, controlling the mass and heat flux.
Plumes hazardous to aviation typically have a deep convective column above the jet.
An umbrella region spreads out atop the column.
Convective columns do not extend above the middle stratosphere.
07/29/26
<number>

## Slide 12
07/29/26
<number>

## Slide 13
Ash clouds can be detected by displaying the Brightness Temperature Difference, Ch 4 - Ch 5 (~11, 12 m) using AVHRR or GOES.
BTD > 0 almost everywhere, as Planck function falls off rapidly as  increases.
However, silica has a strong absorption line near 11 m, so BTD < 0 in elevated ash or dust.
IR signal obscured by thick water clouds, of course, and its absence does not guarantee air free of ash.
07/29/26
<number>

## Slide 14
Grey scale for BTD used here.
Operational monitoring product.
Note use of GMS images.
24 hour sequence.
07/29/26
<number>

## Slide 15
07/29/26
<number>

## Slide 16
07/29/26
<number>

## Slide 17
Warnings are issued by responsible Volcano Observatory staff, including alerts to pilots.
Confirmation of eruption by remote sensing and other techniques are employed urgently.
Plume transport simulations are carried out and results distributed to air traffic controllers.
07/29/26
<number>

## Slide 18
A Lagrangian particle advection model, including turbulent dispersion and gravitational settling.
Column location, height, mass flux are user-specified.
Results are presented in graphical form, either disaggregated (color coded) by height or keyed to specific flight levels.
07/29/26
<number>

## Slide 19
Heights color coded 0 - 16 km.
24 hour simulation.
Plume is “in place” at outset.
07/29/26
<number>

## Slide 20
Event-specific, real time runs.
Fast response for timely warnings.
Specification of location, plume height, etc. Wind data via IDD.
Approximations, most of the judicious.
07/29/26
<number>

## Slide 21
Plume height coverage has been limited by unavailability of winds above 16 km. [Few plumes go that high, and no civilian aircraft do. But particles settle, and we don’t want to be discombobulated by a big event.]
Use of volunteer system seems worrying. NOAA has an operational capability, and one assumes the Air Force does also.
07/29/26
<number>

## Slide 22
Additional sophistication could be developed: dynamic initialization, assimilating remotely-sensed plume characteristics.
A longer term goal could be an integrative threat assessment system. Multi-faceted warnings (seismic, acoustic, surveilance radar, satellite remote sensing).
Warning systems are heterogeneous, another worrying characteristic.
07/29/26
<number>