## Slide 1: Following volcanic ash as a hazard to aviation and as a factor in climate
John Merrill
University of Rhode Island
Graduate School of Oceanography

## Slide 2: Volcanic plumes as hazards to aviation
June, 2003
Expanding Horizons Workshop
<number>
The silicate ash particles in volcanic plumes cause several types of damage to aircraft when encountered during flight.
Operating temperatures in the engines can exceed 1400 C, melting ash particles which then deposit on turbine blades or clog fuel lines.
Engines stalling are a common occurrence. Adept pilots have recovered, even with multiple engine failures.

## Slide 3: Further on hazards to aviation
June, 2003
Expanding Horizons Workshop
<number>
The ash particles also damage the aerodynamic surfaces of aircraft, generally an insidious threat.
~20 flights were in serious danger in the ‘90’s.
Damage to the windscrean is a very common occurrence. Documentation of the frequency and cost of such damage helped spur alert system development.
Coordinated efforts at volcano observatories, forecast offices and air traffic control centers began in the middle ‘90’s.

## Slide 4
June, 2003
Expanding Horizons Workshop
<number>
Routes of some of the 100,000 flight per year in this area.

## Slide 5
June, 2003
Expanding Horizons Workshop
<number>

## Slide 6: Ash transport/dispersal spread risk
June, 2003
Expanding Horizons Workshop
<number>
Many eruptions occur in uninhabited areas, undetected.
Ash clouds can remain airborne for several days.
Spreading of the plume reduces the visual signature and makes discrimination from clouds difficult, particularly at night.
Aircraft radar is ineffective.

## Slide 7: Volcanic plume characteristics
June, 2003
Expanding Horizons Workshop
<number>
Eruptive volcanic plumes occur in numerous forms, varying in height, intensity, duration and in style.
A forced jet occurs at the surface, controlling the mass and heat flux.
Plumes hazardous to aviation typically have a deep convective column above the jet.
An umbrella region spreads out atop the column.
Convective columns do not extend above the middle stratosphere.

## Slide 8: Eruption plume from Mt. Spurr, AK Typical jet-convective-umbrella style
June, 2003
Expanding Horizons Workshop
<number>

## Slide 9: Split-window IR detection
June, 2003
Expanding Horizons Workshop
<number>
Ash clouds can be detected by displaying the Brightness Temperature Difference, Ch 4 - Ch 5 (~11, 12 m) using AVHRR or GOES.
BTD > 0 almost everywhere, as Planck function falls off rapidly as  increases.
However, silica has a strong absorption line near 11 m, so BTD < 0 in elevated ash or dust.
IR signal obscured by thick water clouds, of course, and its absence does not guarantee air free of ash.

## Slide 10: Animated BTD Plume Images Bezymianny volcano, August, 2001
June, 2003
Expanding Horizons Workshop
<number>
Grey scale for BTD used here.
Operational monitoring product.
Note use of GMS images.
24 hour sequence.

## Slide 11
June, 2003
Expanding Horizons Workshop
<number>

## Slide 12
June, 2003
Expanding Horizons Workshop
<number>

## Slide 13: Steps taken after detection
June, 2003
Expanding Horizons Workshop
<number>
Warnings are issued by responsible Volcano Observatory staff, including alerts to pilots.
Confirmation of eruption by remote sensing and other techniques are employed urgently.
Plume transport simulations are carried out and results distributed to air traffic controllers.

## Slide 14: Characteristics of PUFF model
June, 2003
Expanding Horizons Workshop
<number>
A Lagrangian particle advection model, including turbulent dispersion and gravitational settling.
Column location, height, mass flux are user-specified.
Results are presented in graphical form, either disaggregated (color coded) by height or keyed to specific flight levels.

## Slide 15: Bezymianni plume simulation - Puff model
June, 2003
Expanding Horizons Workshop
<number>
Heights color coded 0 - 16 km.
24 hour simulation.
Plume is “in place” at outset.

## Slide 16: Needs met by PUFF and corresponding charactertistics
June, 2003
Expanding Horizons Workshop
<number>
Event-specific, real time runs.
Fast response for timely warnings.
Specification of location, plume height, etc. Wind data via IDD.
Approximations, most of the judicious.

## Slide 17: Prospects and problems
June, 2003
Expanding Horizons Workshop
<number>
Plume height coverage has been limited by unavailability of winds above 16 km. [Few plumes go that high, and no civilian aircraft do. But particles settle, and we don’t want to be discombobulated by a big event.]
Use of volunteer system seems worrying. NOAA has an operational capability, and one assumes the Air Force does also.

## Slide 18: Further prospects
June, 2003
Expanding Horizons Workshop
<number>
Additional sophistication could be developed: dynamic initialization, assimilating remotely-sensed plume characteristics.
A longer term goal could be an integrative threat assessment system. Multi-faceted warnings (seismic, acoustic, surveilance radar, satellite remote sensing).
Warning systems are heterogeneous, another worrying characteristic.

## Slide 19: Climate effects of massive volcanic eruptions
June, 2003
Expanding Horizons Workshop
<number>
Lifetime of ash is limited, especially in the troposphere but even in the stratosphere.
Therefore the radiative impact of ash on climate is minor.
Eruption clouds containing massive amounts of SO2 result in long-lived stratospheric aerosols with lasting effects.

## Slide 20: Other plume types
June, 2003
Expanding Horizons Workshop
<number>
Convective columns do not extend above the middle stratosphere, because a single vent cannot emit sufficient heat or mass to support the column.
Ignimbrite flows can arise from collapsed convective columns or lava pooled on the surface.
The flow can separate where the air becomes superheated and particulates selectively settle out, and the remaining mixture becomes strongly buoyant.
The resulting co-ignimbrite flow can, in extreme cases, extend above the middle stratosphere.

## Slide 21: Case study of Toba volcano
June, 2003
Expanding Horizons Workshop
<number>
The Toba caldera in Sumatra, Indonesia was the site of four massive eruptions since 1.2 MA.
The most recent, 74 kya, resulted in the Youngest Toba Tuff. YTT is found in layers up to 10 m in thickness.
This is the largest known eruption during the Quaternary. About 3000 km3 (dense rock equivalent) was ejected.

## Slide 22: Puff simulation of hypothetical Toba eruption in 2003
June, 2003
Expanding Horizons Workshop
<number>
Column height limited to 16 km.
Importance of UT westerly winds is obvious.

## Slide 23: Further on Toba volcano
June, 2003
Expanding Horizons Workshop
<number>
The eruption column was of co-ignimbrite form, arising from a widespread lake of eruptive material, perhaps > 50 km wide.
The column extended above 45 km, perhaps to the stratopause.
Most of the distal ash has been found in the Indian Ocean and on the subcontinent. Recent results confirm ashfall in the Pacific as well. (Layers misidentified previously, ascribed to other events.)
Investigation of transport scenarios seems needed.

## Slide 24
June, 2003
Expanding Horizons Workshop
<number>
Tropical stratospheric winds vary in intensity and direction.

## Slide 25
June, 2003
Expanding Horizons Workshop
<number>
Alternating winds encroach from above, weakening below 22 km. Quasi-biennial oscillation.

## Slide 26: Climate impacts of Toba eruption
June, 2003
Expanding Horizons Workshop
<number>
Significant cooling must have occurred in the years after the eruption, although the magnitude and duration are open to discussion.
The mass flux is estimated as ~ 1000 x that of Pinatubo (1˚C global cooling for one year) and ~100 x that of Tamboura (1815; 1816 was year “without a summer” in New England).
“A” glacial maximum ensued soon thereafter, despite the unfavorable phase of Milankovitch parameters.

## Slide 27: A brief summary
June, 2003
Expanding Horizons Workshop
<number>
The hazards caused by aircraft flying through regions of active explosive volcanism are reduced through attentive work of people in several disciplines.
Continued development of the warning and modeling systems are needed. Any suspects?
Application of the findings of eruption characterization studies, together with transport modeling, may lead to further insights on the impacts on climate.

## Slide 28: Acknowledgments, inter alia
June, 2003
Expanding Horizons Workshop
<number>
Prof.s Steven Carey and Haraldur Sigurdsson, URI
Dr. Meng Yang Lee, URI/National Taiwan U.
Rorik Petersen and Ken Papp, University of Alaska - Fairbanks.
Bill Rose and his students, Michigan Technological University.
My apology for the plain appearance of these frames.