## Slide 1: Towards Operational Satellite-based Detection and Short Term Nowcasting of Volcanic Ash* *There are research applications as well.
Michael Pavolonis*, Wayne Feltz*, Mike Richards*, Steve Ackerman*, and Andrew Heidinger#
* CIMSS/UW-Madison
# NOAA/NESDIS-Madison
Notes: <number>

## Slide 2: Volcanic Ash work at CIMSS
Key activities:
1). Development of an automated ash detection algorithms that are applicable to a large variety of satellite imagers
2). Pursuing methods to determine ash plume heights based on available spectral information
Thus far, this work has mainly utilized data from operational imagers, since they currently provide the greatest spatial and temporal resolution, which is most important for aviation applications.

## Slide 3: Key Interactions with NOAA
The Extended Clouds from AVHRR (CLAVR-x) system offers one platform for operational implementation of the volcanic ash algorithms (A. Heidinger).
Gridded Solar Insolation Project-full disk (GSIP-fd) offers a similar potential operational platform for the GOES imagers (A. Heidinger).
CLAVR-x and GSIP-fd products include a cloud mask, cloud type, cloud top temperature, LWP, IWP, and much more. Ash products are currently being developed for the research versions of CLAVR-x and GSIP-fd.
We are currently collaborating with the Washington VAAC and Gary Ellrod on these potential options within NOAA.
Notes: <number>
CLAVR-x and GSIP-fd offer potential vehicles to operations.

## Slide 4: I. Volcanic Ash Detection…

## Slide 5: Ash Detection Techniques
Several Techniques have been presented in the literature. For instance:
Reverse absorption (Prata et al., 1989; Yu and Rose, 2002)
SO2 detection using IR measurements in the 7 – 12 um range (Watson et al., 2004)
Image enhancement techniques (Ellrod et al., 2003)

## Slide 6: Why Develop New Techniques?
Unfortunately, none of these techniques, alone, performs universally well (see Tupper et al., 2003).
Thus, there is a need to improve upon these tests and combine several techniques to produce an optimal, rigorously tested, automated ash mask for various sensors.
However, there will always be limitations (i.e. complete obstruction by meteorological cloud, very low ash content plumes, and very small-scale plumes relative to pixel size will still remain problematic).

## Slide 7: Ash Cloud Properties
3.75/0.65 um reflectance ratio should be larger for ash than water or ice clouds.
Split window “reverse absorption” feature

## Slide 8: New Ash Detection Techniques
Strength: Little water vapor dependence.
Weakness: Will not work in sun glint. So far, only defined for water surfaces. Daytime only.
Ash Dominated
Water or Ice Dominated
Ash that is covered by a layer of ice is uniquely detectable.
Strength: Works well everywhere.
Weakness: Only applicable to explosive eruptions. Daytime only.

## Slide 9: Nighttime Ash Detection Techniques
***Nighttime 3.75, 6.5, 11, and 12 um tests are also currently under development.
Meteo. Clouds
Ash Clouds
Clear sky calculation
Linearly roll down from clear sky calculation to 0.0 at 270 K in tropics.
Meteorological and ash cloud simulations support this approach, which is similar to that shown in Yu and Rose (2002).
Atmospherically Corrected Reverse Absorption Technique

## Slide 10: II. Volcanic Plume Height Retrievals…

## Slide 11: Plume Height Estimation Techniques
Shadow techniques (daytime only and under limited conditions)
Aircraft/ground observations (daytime/sparse)
11 um brightness temperature lookup (thick plumes)
Wind correlation (gives a rough estimate)
CO2 slicing (Tony Schreiner/Mike Richards/Steve Ackerman, very promising – see next slide)

## Slide 12
Sheveluch, Russia – August 28, 2000 – Terra/MODIS 2355Z
CO2-slicing yields heights at approximately 10-11 km, video estimate is 14 to 16 km, MODIS is 80 minutes after eruption.
Credit: Mike Richards
Notes: <number>
Collaboration has begun with Russian scientists who monitor volcanic plumes by video and by seismic tremors. This is only an example of the technique used from the video stills. The video height estimates for this case were full of errors, cannot necessarily be trusted, notice non-vertical ash cloud. Video estimates range from 14km to 16km from this image, which was taken 80 minutes prior to MODIS overpass, when the cloud was directly above the volcano. However, this is, in the Sergey’s opinion, ample time for the cloud to drift east and decrease in 4km altitude as shown. Current photo technique may be different. This is circa 2000, and just an example.

## Slide 13: Why Develop New Techniques?
CO2 slicing should provide the best plume height estimate but…
CO2 channels are not available on all current sensors (e.g. MTSAT, GOES-10 imager, AVHRR) and will NOT be available on the MODIS-like VIIRS on NPOESS (2008 and beyond).
There are also no CO2 channels on the AVHRR and the AVHRR will be around until at least 2014.
The VIIRS (0.75 km resolution) and the AVHRR (1-4 km resolution) provide detailed imagery that is useful for identifying volcanic plumes.

## Slide 14: New Plume Height Retrieval (Heidinger and Pavolonis, in prep.)
Results are being validated against MODIS. Goal is to achieve consistency with MODIS and VIIRS for thin cirrus – difficult from AVHRR.
Split window 1DVAR-optimal estimation technique
Cloud top temperature/emissivity are retrieved simultaneously.
Day/night independent.
Currently used in CLAVR-x and GSIP.
MODIS
AVHRR

## Slide 15: Some Results…

## Slide 16
Manam, PNG October 24, 2004
Black = BTD(11 um – 12 um) < 0.0 K

## Slide 17
Manam, PNG October 24, 2004
Darwin VAAC estimated lower plume to be at about 18,000 feet (~5000-6000 m).
*Image area and color scales are different.

## Slide 18
Manam, PNG November 29, 2004
Black = BTD(11 um – 12 um) < 0.0 K

## Slide 19
Manam, PNG November 29, 2004
Darwin VAAC estimated plume to be at about 15,000 feet (~4000-5000 m).

## Slide 20: Mount St. Helens AVHRR Example
VAAC Height up to 11000 m
VAAC Height up to 6000 m
Retrieved heights agree well with VAAC analysis in the thickest regions of the plume.

## Slide 21: False Alarm Rate
This is NOT a suggested product, but it is an effective diagnostic tool.
The ash detection algorithm was applied to 1 day of descending node (mainly daytime) Terra MODIS data. Little or no ash was reported by the VAAC’s on this day (April 4, 2003). A closer examination of pixel level data reveals that most false alarms were caused by water cloud edges.
Notes: <number>
It is not only important to test the algorithm on scenes where ash is known to be present, but also on scenes when ash is NOT present.

## Slide 22: False Alarm Rate
Here is what the false alarm rate looks like is you use the following test for ash:
BTD (11 um – 12 um) < 0.0 K (30oS-30oN)
BTD (11 um – 12 um) < -0.2 K (elsewhere)
Bottom line: the reverse absorption technique is often useful, but should be supplemented with additional spectral information for optimal results.
Notes: <number>
The technique presented here was shown to be more sensitive to the presence of ash for the scenes analyzed, but also less prone to false alarms.

## Slide 23: Hyperspectral Sounder Applications
Hyperspectral IR sounders offer increased sensitivity to the presence individual volcanic aerosols (e.g. SO2, H2SO4, particulate ash, etc…).
Thus the retrieval of plume composition, height, particle size, and emissivity can be performed more accurately. This has been shown to some degree with AIRS and the current GOES Sounder, but much work remains.
The future of operational and research-based volcanic ash applications is promising given the expected increase in hyperspectral instruments in orbit.
Notes: <number>
Important for dispersion modeling.

## Slide 24: Backup Slides

## Slide 25: Split Window vs CO2 Slicing (meteorological clouds)
Likely due to a recent bug found in the MODIS algorithm.
Very thin clouds (emissivity < 0.5)
**Some differences may be due to 20 minute time difference between MODIS and AVHRR overpass.
Notes: <number>
Only for the very thinnest of clouds, the MODIS is superior. Split window technique is likely better than IR lookup for low clouds.

## Slide 26
MODIS Co2 Heights
MISR No Wind
Correction Heights
MISR With Wind
Correction Heights
Etna, Oct. 27, 2002 TERRA 1000Z
Credit: Mike Richards

## Slide 27: Current Imagers
GEO: GOES-9, GOES-10, GOES-12, MSG, and MTSAT-1R
LEO: AVHRR, ATSR-2, and MODIS
MODIS and MSG have the best spectral capabilities. But…
With the exception of GOES-12, all of the above have visible (0.65 um), near-infrared (1.6 um or 3.8 um), 11 um, and 12 um channels, which are vital for automated ash detection.
GOES-12 does not have a 12 um channel.

## Slide 28: Future Work
Continue collaboration with Gary Ellrod and SAB.
Continue algorithm refinement/characterization and “validation” while keeping in mind the global aspect of the problem.
Develop quality flags.
Utilize hyperspectral data to perform more detailed volcanic plume retrievals.

## Slide 29: Comparison to MODIS CO2
Darwin VAAC estimated lower plume to be at about 18,000 feet (~5000-6000 m).
**Image area and color scales are different.

## Slide 30: CO2 Slicing Summary
Initial investigation looks promising
CO2 appears to be too low, as with clouds, since it retrieves an radiative height
How to increase heights?
  Emissivity adjustments
  Error in assumed profiles
  Statistical adjustment through calculations
  Improve upper limit restrictions
Validation continues, and simulation study begun.
Additional examples will be shown later.

## Slide 31: Comparison to MODIS CO2
Darwin VAAC estimated plume to be at about 15,000 feet (~4000-5000 m).
**Image area and color scales are different.