## Slide 1
Encounters of Aircraft with Volcanic-Ash Clouds:
An Overview
Marianne Guffanti, Thomas Casadevall, and Gari Mayberry
U.S. GEOLOGICAL SURVEY

## Slide 2: Information about ash/aircraft encounters documents the nature and extent of the risk to aviation and helps to refine mitigation efforts.
Additional data about encounters confirms recommended pilot actions in the event of an encounter and may lead to further refinements.
Models of ash dispersion can be refined.
Weaknesses in communication links can be identified and fixed.
Training needs can be pinpointed.
Notes: <number>

## Slide 3: Summary of reported encounters published in 2001 in ICAO Manual on Volcanic Ash, Radioactive Material & Toxic Chemical Clouds put together by Tom Casadevall (USGS) and Tom Fox (ICAO)
83 encounters from 1935 to 1993 are listed, along with information on the source volcanoes, eruption dates, aircraft types, and severity of the encounters.
Preliminary mention of approximately another ~17 encounters from 1994 to 2000 in accompanying table.
Additional 6 encounters known through 2003 & not in Manual. Most recent reported incident is July 2003 in Caribbean region.
Notes: <number>

## Slide 4
SEVERITY OF ENCOUNTER
Class 0: acrid odor, electrostatic discharge
Class 1: light cabin dust, EGT fluctuations
Class 2: heavy cabin dust, ext. & int. abrasion damage,
window frosting,
Class 3: engine vibration, erroneous instrument readings,
hydraulic-fluid contamination, damage to engine
and electrical system
Class 4: engine failure requiring in-flight restart
Class 5: engine failure or other damage leading to crash
NO CLASS 5 ENCOUNTERS TO DATE
From 1973 through 2003, 102 encounters have been reported – minimum value because incidents are not consistently reported publicly.

## Slide 5
Most encounters (~75%) are Class 0-2
Class 4 Encounters:
7 cases involving temporary engine failure occurred from 1980-1991.
Encounters happened 150 to 600 miles from volcanic sources (St. Helens, Galunggung, Redoubt, Pinatubo, Unzen).
Durations of encounters from 2 to 13 minutes.
In-flight multiple-engine failure in modern planes is extremely rare. Ash is main culprit.
(One other case due to fuel loss in 2000?)

## Slide 6
*** Indonesia, 1982: 25,000 ft and 16 min. of powerless descent ***
B-747, 231 passengers
1989 Redoubt Eruption
ALL ENGINES FAILED
4 min. of powerless descent over mtn. terrain
Notes: <number>

## Slide 7: Encounter Frequency, 1973 – 2003
Pinatubo 1991
~2 encounters/yr (minimum) since Pinatubo
Pinatubo
15 June 91
Notes: <number>

## Slide 8
30 Volcanic Sources of Ash Clouds Encountered Since 1973

## Slide 9
Volcanoes with highest number of encounters (>5):
Pinatubo, Philippines (1991)
Sakura-jima, Japan (1977-1998)
St. Helens, USA (1980)
Augustine, USA (1976)
Redoubt, USA (1989-1990)
Galunggung, Indonesia (1982)
For a given volcano, encounter severity may be: limited to a particular class (e.g, Sakura-jima, class 2) or range widely (e.g., Pinatubo and Redoubt, class 0 to 4).
747 is aircraft type most often involved in encounters – because it has been most commonly used aircraft in transoceanic flights over volcanic regions.

## Slide 10: Encounters result from large and small eruptions
Pinatubo, Philippines, 1991
400 miles across
Soufriere Hills,
Montserrat, 2003
Notes: <number>

## Slide 11
The USGS & Smithsonian Institution, in collaboration with Darwin VAAC, will continue to maintain a summary of reported encounters in the form of a queriable database that includes information about the source eruptions and encounter conditions.
Data identifying the airlines or aircraft operators involved in encounters will not be included in the database.
An updated summary of encounters will be provided to ICAO for publication in a future update of the 2001 Manual.

## Slide 12: Encounter Database Fields:
unique incident number
encounter date and time
encounter lat/long and altitude
aircraft type (not airline)
severity of encounter
damages and costs
volcanic source, lat/long, Smithsonian ID number
eruption date, time, duration, and column height
volcanic explosivity index
flight route info
distance of encounter from volcanic source
time between eruption and encounter
source of satellite imagery
issuance of SIGMETs and VAAs
references

## Slide 13
To ATS via radio & at next point of landing.
Also Smithsonian via email (gvn@volcano.si.edu)
gvn@volcano.si.edu
Notes: <number>

## Slide 14
ICAO Doc 4444 and Annex 3 refer to the VOLCANIC ACTIVITY REPORT (VAR) and provide a format.
The issue is getting cooperation from pilots and Air Traffic Services to complete these reports and forward them to appropriate services and agencies for operational use and historical record-keeping (by the USGS & Smithsonian).
Reporting Encounters:

## Slide 15
Near loss of fully loaded passengers jets caused people to act. Existing systems were adapted & missions evolved.
Better tracking of ash clouds and faster, more reliable communication became possible with advances in technology.
Fewer encounters (normalized for increased traffic) & lower severity; no crashes.
MITIGATION WORKS
But Imperfectly …..
Encounters have continued.
Notes: <number>

## Slide 16: Why do encounters continue to occur?
Unexpected eruptions at unmonitored volcanoes; incomplete eruption reporting
Limitations in methods of detecting ash clouds, including the time it takes to get satellite data.
Limitations in forecasting cloud dispersion
Breakdowns in information dissemination
Inadequate training and hazard awareness

## Slide 17
GLOBAL STRATEGY: quickly communicate information about explosive eruptions & locations of ash clouds to ATC, dispatchers, & pilots so clouds can be avoided.
INVOLVED PARTIES:
    Airlines
    Air Traffic Agencies
    National Weather Services
    Scientists (Volcanologists, Meteorologists)
    WMO, ICAO, ALPA, etc.
MITIGATION ELEMENTS:
1 – Volcano Monitoring & Eruption Reporting
2 – Ash Cloud Detection
3 – Forecasting Cloud Movement
4 – Communication
5 – Hazard Awareness
Volcanic ash will persist as a serious aviation hazard: heavy traffic over volcanic regions, free-flight routing, ETOPS, larger hotter engines.
Notes: <number>

## Slide 18: Resist complacency: A perverse aspect of effective mitigation is that the prevention of bad outcomes can lead to an unwarranted complacency that the underlying hazard has been eliminated. As our ability to prevent encounters improves to the point that even fewer incidents occur, we must not mistakenly conclude that no threat exists, but rather call for continued vigilance and support of broad-based mitigation capabilities.
Notes: <number>

## Slide 19
NASA Shuttle image of 1994 eruption of Rabaul Volcano, PNG